## Slide 1: Complex dynamics of a microwave time-delayed feedback loop
Hien Dao
September 4th , 2013
PhD Thesis Defense
Chemical Physics Graduate Program
Prof. Thomas Murphy - Chair
Prof. Rajarshi Roy
Dr. John Rodgers
Prof. Michelle Girvan
Prof. Brian Hunt – Dean Representative
Committee:

## Slide 2: Outline
Introduction:
    Deterministic chaos
    Deterministic Brownian motion
    Delay differential equations
Microwave time-delayed feedback loop:
    Experimental setup
    Mathematical model
    Complex dynamics:
    - The loop with sinusoidal nonlinearity: bounded and unbounded dynamics regimes
    - The loop with Boolean nonlinearity
Potential applications:
    - Range and velocity sensing
Conclusion
Future works
Notes: Here is the outline of the talk. In the first part, I will give out the general introduction on deterministic chaos, deterministic B motion and delay differential equations. Through the introductory information, I will draw the motivation of the research subject. I will then move on to talk about …, how we setup the experimental system, how we model the loop and the complex dynamics we could observe in the loop. I also will address significant of the result by demonstrating the potential range and velocity sensing application using FM chaotic signal generated by the loop. I conclude the talk by presenting conclusion and propose future research.

## Slide 3: Introduction :
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
  Lorenz attractor
  Wikipedia
Motion of double compound pendulum
The distribution of dye in a fluid http://www.chaos.umd.edu/gallery.html
  Wikipedia
‘‘An aperiodic long term behavior of a bounded deterministic system that exhibits sensitive dependence on initial conditions’’ – J. C. Sprott, Chaos and Time-series Analysis
Universality
Applications:
- Communication G. D. VanWiggeren, and R. Roy, Science 20, 1198 (1998)
- Encryption L. Kocarev, IEEE Circ. Syst. Mag 3, 6 (2001)
- Sensing, radar systems J. N. Blakely et al., Proc. SPIE 8021, 80211H (2011)
- Random number generation A. Uchida et al., Nature Photon. 2, 728 (2008)
-…
Chaos
Quantifying chaos
Type of chaotic signal
Microwave chaos
Notes: The general definition of chaos states that chaos is aperiodic long term behaviorof a bounded deternministics systsm that exhibit the sen.. The first well known example of chaos is Lorenz system. While working on modeling the weather system, he discovered that a set of three first order, coupled nonlinear equations could display the aperiodic solution. This solution is never setlle down to an equilibrium or periodic state instead it continues to oscillate in aperiodic fashion. If the simukation starts from slightly different I c, the trajectories could be strongly divert. Nowadays, it is clear that one could observe this chaotic behavior in most branches of science. The two example shown here are from fluid dynamics and mechanics. The uniqueness and universality of chaos can bring it to different applications, such as

## Slide 4: Introduction :
Lyapunov exponents and
The quantity whose sign indicates chaos and its value measures the rate at which initial nearby trajectories exponentially diverge.
- A positive maximal Lyapunov exponent is a signature of chaos.
Power spectrum
- Broadband behavior
Power spectrum of a damp, driven pendulum’s aperiodic motion
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Chaos
Quantifying chaos
Type of chaotic signal
Microwave chaos
Kaplan – Yorke dimensionality
Kaplan-Yorke dimension: fractal dimensionality

## Slide 5
Chaotic signal
Chaos in amplitude or envelope
Chaos in phase or frequency!!
A.B. Cohen et al, PRL 101, 154102 (2008)
Lorenz system’s chaotic solution
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Chaos
Quantifying chaos
Type of chaotic signals
Microwave chaos
x (t)
Time
Introduction :
Demonstration of a frequency-modulated signal

## Slide 6
Modern communication: cell-phones, Wi-Fi, GPS, radar, satellite TV, etc…
Advantages of chaotic microwave signal:
  Wider bandwidth and better ambiguity diagram
  Reduced interference with existing channels
  Less susceptible to noise or jamming
Global Positioning System
http://www.colorado.edu/geography/gcraft/notes/gps/gps_f.html
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Chaos
Quantifying chaos
Type of chaotic signals
Microwave chaos
Introduction :
Frequency modulated chaotic microwave signal.

## Slide 7
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Definition
Properties
Hurst exponents
Brownian motion:
Deterministic Brownian motion:
A random movement of microscopic particles suspended in liquids or gases resulting from the impact of molecules of the surrounding medium
A macroscopic manifestation of the molecular motion of the liquid
Simulation of Brownian motion - Wikipedia
Introduction :
A Brownian motion produced from a deterministic process without the addition of noise

## Slide 8
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Definition
Properties
Hurst exponents
Gaussian distribution of the displacement over a given time interval.
Introduction :
0
40
80
120
4
-4
0
Bins width
Probability distribution

## Slide 9
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Definition
Properties
Hurst exponents
Introduction :
H = 0.5 regular Brownian motion
H < 0.5 anti-persistence Brownian motion
H > 0.5 persistence Brownian motion
1.6
2
2.4
2.8
H = 0.57
0.4
0.8
1.2
H: Hurst exponent
0 < H < 1
Fractional Brownian motions:

## Slide 10: Introduction :
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Ikeda system
Mackey-Glass system
Optoelectronic system
A.B. Cohen et al, PRL 101, 154102 (2008)
Y. C. Kouomou et al, PRL 95, 203903 (2005)
K. Ikeda and K. Matsumoto, Physica D 29, 223 (1987)
M. C. Mackey and L. Glass, Science 197, 287 (1977)
History
System realization
Chaos is created by nonlinearly mixing one physical variable with its own history.

## Slide 11: Introduction :
Deterministic chaos
Deterministic Brownian motion
Delay differential equations
Nonlinearity
Delay
Filter function
Nonlinearity
Filter
Gain
Delay
x(t)
History
System realization
“…To calculate x(t) for times greater than t, a function x(t) over the interval (t, t - t) must be given. Thus, equations of this type are infinite dimensional…”
J. Farmer et al, Physica D 4, 366 (1982)
Time-delayed feedback loop

## Slide 12: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics

## Slide 13: Microwave time-delayed feedback loop:
Voltage Controlled Oscillator
Baseband signal
FM Microwave signal
Mini-circuit VCO
SOS-3065-119+
Experimental setup
Mathematical model
Complex dynamics

## Slide 14: Microwave time-delayed feedback loop:
varies slowly on the time scale
A homodyne microwave phase discriminator
Experimental setup
Mathematical model
Complex dynamics

## Slide 15: Microwave time-delayed feedback loop:
Nonlinear function
A printed- circuit board microwave generator
Experimental setup
Mathematical model
Complex dynamics

## Slide 16: Microwave time-delayed feedback loop:
Field Programmable Gate Array board
Sampling rate: Fs = 75.75 Msample/s
2 phase-locked loop built in
8-bit ADC
10-bit DAC
Experimental setup
Mathematical model
Complex dynamics
Altera Cyclone II
FX2 USB port
Output
Input
DAC
FPGA chip
ADC

## Slide 17: Microwave time-delayed feedback loop:
Memory buffer with length N to create delay t
Experimental setup
Mathematical model
Complex dynamics
Discrete map equation for filter function
H(s)
H(z)
Discrete map equation
T: the integration time constant

## Slide 18: Microwave time-delayed feedback loop:
M. Schanz et al., PRE 67, 056205 (2003)
J. C. Sprott, PLA 366, 397 (2007)
The ‘simplest’ time-delayed differential equation
Experimental setup
Mathematical model
Complex dynamics

## Slide 19: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Experimental setup
Mathematical model

## Slide 20: Microwave time-delayed feedback loop:
Simulation
5th order Dormand-Prince method
Random initial conditions
Pre-iterated to eliminate transient
t= 40 ms
R is range from 1.5 to 4.2
Parameter | Value
sampling rate | 15 MS/s
N | 600
A | 0.2V
v2p | 0.5V
g | 180 MHz/V
w0/2p | 2.92 GHz
a (40-bit) | 0.0067-0.0175
scope
Experiment
Experimental setup
Mathematical model
Complex dynamics

## Slide 21: Microwave time-delayed feedback loop:
Low feedback strength generated periodic behavior.
Period: 4t (6.25kHz)
R = p/2
Experimental setup
Mathematical model
Complex dynamics

## Slide 22: Microwave time-delayed feedback loop:
Intermediate feedback strength generated: More complicated but still periodic behavior.
R = 4.1
Experimental setup
Mathematical model
Complex dynamics

## Slide 23: Microwave time-delayed feedback loop:
High feedback strength: Chaotic behavior.
Irregular, aperiodic but still deterministic.
lmax = +5.316/t , DK-Y = 2.15
R = 4.176
Experimental setup
Mathematical model
Complex dynamics

## Slide 24: Microwave time-delayed feedback loop:
baseband
microwave
Experimental setup
Mathematical model
Complex dynamics
Power spectra

## Slide 25: Microwave time-delayed feedback loop:
Period-doubling route to chaos
Experimental setup
Mathematical model
Complex dynamics
Bifurcation diagrams
Notes: Remind what the axes are?

## Slide 26: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Positive lmax indicates chaos.
Maximum Lyapunov exponents

## Slide 27: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Another nonlinearity

## Slide 28: Microwave time-delayed feedback loop:
Time traces and time-embedding plot
No fixed point solution
Always periodic
Amplitudes are linearly dependence on system gain R
R >3p/2, the random walk behavior occurs (not shown)
Experimental setup
Mathematical model
Complex dynamics
Notes: Amplitude continues to grow in proportion to R but the trajectory acquire secondary peaks on the rising and falling

## Slide 29: Microwave time-delayed feedback loop:
Bifurcation diagrams
Periodic, but self-similar!
(c) is a zoomed in version of the rectangle in (b)
(d) Is a zoomed in version of the rectangle in (c).
Experimental setup
Mathematical model
Complex dynamics

## Slide 30: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Unbounded dynamics regime
Yttrium iron garnet (YIG) oscillator
Delay td is created using K-band hollow rectangular wave guide
The system reset whenever the signal is saturated
R > 4.9

## Slide 31: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Experimental observed deterministic random motion
Tuning voltage time series
Distribution function of displacement
Hurst exponent estimation
The tuning signal exhibits Brownian motion!

## Slide 32: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Numerically computed
Experimental estimated
I
*
The tuning signal could exhibit fractional Brownian motion.
The system shows the transition from anti-persistence to regular to persistence Brownian motion as the feedback gain R is varied

## Slide 33: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Synchronization of deterministic Brownian motions
Unidirectional coupling in the baseband
System equations
Master
Slave
The systems are allowed to come to the statistically steady states before the coupling is turned on

## Slide 34: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Simulation results
The master system could drives the slave system to behave similarly at different cycle of nonlinearity.
The synchronization is stable.
Evolution of synchronization perturbation vector

## Slide 35: Microwave time-delayed feedback loop:
Experimental setup
Mathematical model
Complex dynamics
Synchronization error s
Where:
The synchronization ranges depends on the feedback strength R.
Simulation results

## Slide 36: Potential Applications
Range and velocity sensor
Random number generator
GPS: using PLL to track FM microwave chaotic signal

## Slide 37: Potential Applications:
Pulse radar system - Wikipedia
Doppler radar- Wikipedia
Objective: Unambiguously determine position and velocity of a target.
Can we use the FM chaotic signal for S(t)?
S(t)
S(t)
rS(t-t)
Range and velocity sensing application
Ambiguity function
Experimental FM chaotic signal

## Slide 38: Potential Applications:
Formula:
Ideal Ambiguity Function
Ambiguity function for FM signals
- Approximation and normalization
Fixed Point
Periodic
Chaotic
Range and velocity sensing application
Ambiguity function
Experimental FM chaotic signal

## Slide 39: Potential Applications:
Broadband behavior at microwave frequency
Experiment
Simulation
Spectrum of FM microwave chaotic signal
2.9 GHZ
52 MHz
15dB/div
Range and velocity sensing application
Ambiguity function
Experimental FM chaotic signal
Chaotic FM signals shows significant improvement in range and velocity sensing applications.
-3
3
0

## Slide 40: Conclusion (1)
Designed and implemented a nonlinear microwave oscillator as a hybrid discrete/continuous time system
Developed a model for simulation of experiment
Investigated the dynamics of the system with a voltage integrator as a filter function
    A bounded dynamics regime:
        Sinusoidal nonlinearity: chaos is possible
        Boolean nonlinearity: self-similarity periodic behavior
    An unbounded dynamics regime: deterministic Brownian motion

## Slide 41: Conclusion (2)
Generated FM chaotic signal in frequency range : 2.7-3.5 GHz
Demonstrated the advantage of the frequency-modulated microwave chaotic signal in range finding applications

## Slide 42: Future work
Frequency locking (phase synchronization) in FM chaotic signals
Network of periodic oscillators
The feedback loop with multiple time delay functions

## Slide 43
Thank you!

## Slide 44: Supplementary materials

## Slide 45
Calculate ambiguity function of Chaos FM signal
Ambiguity function: the 2-dimensonal function of time delay t and Doppler frequency f showing the distortion of the returned signal;
The value of ambiguity function is given by magnitude of the following integral
Where s(t) is complex signal, t is time delay and f is Doppler frequency
Chaos FM signal:
Approximation:
where
(operating point)

## Slide 46
L/N
L/N
L/N
C/2N
C/2N
C/2N
C/2N
C/2N
C/2N
N units
L=5 mH
C=1nF
tu=0.1 ms/unit;
= 1.2 ms
fcutoff ~ 3 MHz
Loop feedback delay t is built in with transmission line design
Notes: Move to the back, appendix slides for questions.

## Slide 47: Simulation Results
1
2
3
4
6
5
7
b
-2
2
0
20
10
0
0
-0.4
0.4
20
10
0
Time [ms]
0
-0.6
0.6
20
Time [ms]
10
0
-1.5
2
Time [ms]
X(t)
X
Bifurcation Diagram
b = 1.6
b = 2.7
b = 6.2

## Slide 48
-2
2
0
V
Bifurcation Diagram
Experiment
Spectral diagram
of microwave signal
Frequency [GHz]
3
3.1
3.2
2.9
2.8
2.7
Notes: Explain what is bifurcation diagram is? Spectral diagram? What kind of dynamical behaviors we can observe? What does it tell us about system?

## Slide 49: Coupling and Synchronization
bias
VCO
splitter
td
mixer
t
H(s)
v1(t)
b
bias
VCO
splitter
td
mixer
t
H(s)
v2(t)
b
k
k : coupling strength
(I)
(II)
Two systems are coupled in microwave band within or outside of filter bandwidth
Two possible types of synchronization:
- Baseband Envelope Synchronization
- Microwave Phase Synchronization
Notes: Why we need to get phase synchronization? What are advantages of that in communication/ control theory? Coupling equation and pointing out what parameter will be compared; what are flexible parameters, i.c to put systems into different regimes; giving some examples about ES and PS done w different systems ;

## Slide 50: Experimental Results Unidirectional coupling, outside filter bandwidth, k = 0.25
b = 1.2
b = 5.1
0
5
10
15
20
0
5
10
15
20
V1(t)
V2(t)
V1(t)-V2(t)
V1(t)
V2(t)
V1(t)-V2(t)
0
1
-1
0
-5
5
Time [ms]
Time [ms]

## Slide 51: Experimental Results Bidirectional coupling, outside filter bandwidth, k = 0.35
b = 1.2
b = 2.1
0
5
10
15
20
0
5
10
15
20
V1(t)
V2(t)
V1(t)-V2(t)
V1(t)
V2(t)
V1(t)-V2(t)
0
1
-1
0
2
-2
Time [ms]
Time [ms]

## Slide 52
Transmission line for VCO system?
* Microstrip line with characteristic impedance 50 Ohm
Dielectric material: Roger 4350B with
* Using transmission line to provide certain delay time in RF range

## Slide 53
Using HFSS to calculate the width of transmission line and simulate the field on transmission line
Width of trace: 0.044’’ thickness of RO3450 : 0.02”; simulation done with f=5GHz

## Slide 54
Printed Circuit Board of VCO system

## Slide 55
Distance Radar
Idea:
VCO
integrator
t
scope
Using microwave signal generated by VCO for detecting position of object in a cavity
Mathematical model:
Nonlinearity
V2p
V0
In general
In particular case has been investigated
RF delay and nonlinearity
Transmission line

## Slide 56
Gain =2.5
Gain =3.77
Gain =4.137
How much chances we can detect?

## Slide 57
VCO
integrator
t
scope
Assumption:
is in order of 10-9
Approximated equation:
Continuously change td
Normalization:
Watching dynamics of system, can we determine w (and then z?)

## Slide 58
Using PLL to track chaotic FM signal
VCO
integrator
scope
Chaos Generator
Chaotic FM signal
vp
Mixer output
vpm
Always can pick
Integrator equation
Or another filter function?
[A2]: voltage as Vp-p
PLL equation

## Slide 59
Does solution exist?
Chaos generator
Equations:
In general case, bc and bp could be assumed to be different by some scaling factor bc/bp = n
Static = time evolution ?!